## Slide 1: Folklore Confirmed: Compiling for Speed = Compiling for Energy
Tomofumi Yuki INRIA, Rennes
Sanjay Rajopadhye Colorado State University

## Slide 2: Exa-Scale Computing
Reach 1018 FLOP/s by year 2020
Energy is the key challenge
  Roadrunner (1PFLOP/s): 2MW
  K (10PFLOP/s): 12MW
  Exa-Scale (1000PFLOP/s): 100s of MW?
Need 10-100x energy efficiency improvements
What can we do as compiler designers?

## Slide 3: Energy = Power × Time
Most compilers cannot touch power
  Go as fast as possible is energy optimal
Also called “race-to-sleep” strategy
Dynamic Voltage and Frequency Scaling
  One knob available to compilers
  Control voltage/frequency at run-time
  Higher voltage, higher frequency
  Higher voltage, higher power consumption
Notes: Also mention many compiler optimizations, e.g., locality, also contribute to less power

## Slide 4: Can you slow down for better energy efficiency?
Yes—in Theory
  Voltage scaling:
    Linear decrease in speed (frequency)
    Quadratic decrease in power consumption
    Hence, going slower is better for energy
No—in Practice
  System power dominates
  Savings in CPU cancelled by other components
    CPU dynamic power is around 30%

## Slide 5: Our Paper
Analysis based on high-level energy model
  Emphasis on power breakdown
  Find when “race-to-sleep” is the best
  Survey power breakdown of recent machines
Goal: confirm that sophisticated use of DVFS by compilers is not likely to help much
  e.g., analysis/transformation to find/expose “sweet-spot” for trading speed with energy
Notes: You can also mention that I was going towards this direction for a while during my thesis, and gave up due to this observation.
The emphasis is on “confirm”; say that the observation itself is not new, and has been verified in specific machine with actual power measurements before.
In this paper, we do not look at details of an individual machine, but rather look at general “trends” in computer systems.

## Slide 6: Outline
Introduction
Proposed Model (No Equations!)
  Power Breakdown
  Ratio of Powers
  When “race-to-speed” works
Survey of Machines
DVFS for Memory
Conclusion

## Slide 7: Power Breakdown
Dynamic (Pd)—consumed when bits flips
  Quadratic savings as voltage scales
Static (Ps)—leaked while current is flowing
  Linear savings as voltage scales
Constant (Pc)—everything else
  e.g., memory, motherboard, disk, network card, power supply, cooling, …
  Little or no effect from voltage scaling
Notes: 180nm: 95% was dynamic
32nm: more than 50% is static

## Slide 8: Influence on Execution Time
Voltage and Frequency are linearly related
  Slope is less than 1
  i.e., scale voltage by half, frequency drop is less than half
Simplifying Assumption
  Frequency change directly influence exec. time
  Scale frequency by x, time becomes 1/x
  Fully flexible (continuous) scaling
    Small set of discrete states in practice

## Slide 9: Ratio is the Key
Case1: Dynamic Dominates
  Power 
  Time 
Case2: Static Dominates
  Power 
  Time 
Case3: Constant Dominates
  Power 
  Time 
Pd : Ps : Pc
Pd : Ps : Pc
Pd : Ps : Pc
Pd : Ps : Pc
Energy 
Slower the Better
Energy 
No harm, but No gain
Energy 
Faster the Better

## Slide 10: When do we have Case 3?
Static power is now more than dynamic power
  Power gating doesn’t help when computing
Assume Pd = Ps
  50% of CPU power is due to leakage
    Roughly matches 45nm technology
    Further shrink = even more leakage
The borderline is when Pd = Ps = Pc
  We have case 3 when Pc is larger than Pd=Ps
Notes: It worked out beautifully to Pd = Ps = Pc, but it is by coincidence. The root of the nice cancellation is the equation that relates voltage and frequency: V = 2f/3 + 1/3,
and the assumption Pd = Ps.

## Slide 11: Extensions to The Model
Impact on Execution Time
  May not be directly proportional to frequency
  Shifts the borderline in favor of DVFS
    Larger Ps and/or Pc required for Case 3
Parallelism
  No influence on result
  CPU power is even less significant than 1-core
    Power budget for a chip is shared (multi-core)
    Network cost is added (distributed)

## Slide 12: Outline
Introduction
Proposed Model (No Equations!)
Survey of Machines
  Pc in Current Machines
  Desktop and Servers
  Cray Supercomputers
DVFS for Memory
Conclusion

## Slide 13: Do we have Case 3?
Survey of machines and significance of Pc
Based on:
  Published power budget (TDP)
  Published power measures
  Not on detailed/individual measurements
Conservative Assumptions
  Use upper bound for CPU
  Use lower bound for constant powers
  Assume high PSU efficiency
Notes: PSU efficiency is assumed to be 85% for desktop, 90% for servers, 95% for supercomputers. 85% PSU is already pretty expensive.
Other studies have tried to do this by measuring empirically on a handful of machines. Infeasible (uninteresting) for us to extend
to many machines. Rather we wanted to study the broad trends and stay “high-level.”

## Slide 14: Pc in Current Machines
Sources of Constant Power
  Stand-By Memory (1W/1GB)
    Memory cannot go idle while CPU is working
  Power Supply Unit (10-20% loss)
    Transforming AC to DC
  Motherboard (6W)
  Cooling Fan (10-15W)
    Fully active when CPU is working
Desktop Processor TDP ranges from 40-90W
  Up to 130W for large core count (8 or 16)

## Slide 15: Sever and Desktop Machines
Methodology
  Compute a lower bound of Pc
  Does it exceed 33% of total system power?
  Then Case 3 holds even if the rest was all consumed by the processor
System load
  Desktop: compute-intensive benchmarks
  Sever: Server workloads (not as compute-intensive)

## Slide 16: Desktop and Server Machines
Notes: The majority crosses the bar even with very conservative analysis.
The cluster of servers

## Slide 17: Cray Supercomputers
Methodology
  Let Pd+Ps be sum of processors TDPs
  Let Pc be the sum of
    PSU loss (5%)
    Cooling (10%)
    Memory (1W/1GB)
  Check if Pc exceeds Pd = Ps
  Two cases for memory configuration (min/max)
Notes: Cooling is LB estimate from Oakridge report

## Slide 18: Cray Supercomputers
Chart: 
| XT5 (min) | XT5 (max) | XT6 (min) | XT6 (max) | XE6 (min) | XE6 (max)
CPU-dynamic | 28.5 | 21.5 | 24.5 | 20.5 | 24.5 | 20.5
CPU-static | 28.5 | 21.5 | 24.5 | 20.5 | 24.5 | 20.5
Memory | 5 | 7 | 7 | 11 | 7 | 23
PSU+Cooling | 15 | 15 | 15 | 15 | 15 | 15
Other | 23 | 35 | 29 | 33 | 29 | 21
Notes: 100% line is from published power consumption by Cray
With large memory configuration, the condition is already met.
For others, only a few extra % of constant power is needed to meet the condition, which can easily come from motherboards, networks, disks, and so on.

## Slide 19: Cray Supercomputers
Chart: 
| XT5 (min) | XT5 (max) | XT6 (min) | XT6 (max) | XE6 (min) | XE6 (max)
CPU-dynamic | 28.5 | 21.5 | 24.5 | 20.5 | 24.5 | 20.5
CPU-static | 28.5 | 21.5 | 24.5 | 20.5 | 24.5 | 20.5
Memory | 5 | 7 | 7 | 11 | 7 | 23
PSU+Cooling | 15 | 15 | 15 | 15 | 15 | 15
Other | 23 | 35 | 29 | 33 | 29 | 21
Notes: 100% line is from published power consumption by Cray
With large memory configuration, the condition is already met.
For others, only a few extra % of constant power is needed to meet the condition, which can easily come from motherboards, networks, disks, and so on.

## Slide 20: Cray Supercomputers
Chart: 
| XT5 (min) | XT5 (max) | XT6 (min) | XT6 (max) | XE6 (min) | XE6 (max)
CPU-dynamic | 28.5 | 21.5 | 24.5 | 20.5 | 24.5 | 20.5
CPU-static | 28.5 | 21.5 | 24.5 | 20.5 | 24.5 | 20.5
Memory | 5 | 7 | 7 | 11 | 7 | 23
PSU+Cooling | 15 | 15 | 15 | 15 | 15 | 15
Other | 23 | 35 | 29 | 33 | 29 | 21
Notes: 100% line is from published power consumption by Cray
With large memory configuration, the condition is already met.
For others, only a few extra % of constant power is needed to meet the condition, which can easily come from motherboards, networks, disks, and so on.

## Slide 21: Outline
Introduction
Proposed Model (No Equations!)
Survey of Machines
DVFS for Memory
  Changes to the model
  Influence on “race-to-sleep”
Conclusion

## Slide 22: DVFS for Memory (from TR version)
Still in research stage (since 2010~)
Same principle applied to memory
  Quadratic component in power w.r.t. voltage
    25% quadratic, 75% linear
The model can be adopted:
  Pd becomes Pq dynamic to quadratic
  Ps becomes Pl static to linear
The same story but with Pq : Pl : Pc
Notes: The conclusion is that DVFS for memory may provide opportunities for slowing down to be more energy efficient, but only for a short time unless the leakage problem is solved.
At current rate, leakage will probably be dominant by the time DVFS for memory gets implemented.

## Slide 23: Influence on “race-to-sleep”
Methodology
  Move memory power from Pc to Pq and Pl
    25% to Pq and 75% to Pl
  Pc becomes 15% of total power for Server/Cray
    “race-to-sleep” may not be the best anymore
    remains to be around 30% for desktop
  Vary Pq:Pl ratio to find when “race-to-sleep” is the winner again
    leakage is expected to keep increasing

## Slide 24: When “Race to Sleep” is optimal
When derivative of energy w.r.t. scaling is >0
dE/dF
Linearly Scaling Fraction: Pl / (Pq + Pl)

## Slide 25: Outline
Introduction
Proposed Model (No Equations!)
Survey of Machines
DVFS for Memory
Conclusion

## Slide 26: Summary and Conclusion
Diminishing returns of DVFS
  Main reason is leakage power
  Confirmation by a high-level energy model
  “race-to-speed” seems to be the way to go
  Memory DVFS won’t change the big picture
Compilers can continue to focus on speed
  No significant gain in energy efficiency by sacrificing speed
Notes: Note that it is the ratio of dynamic : static : constant, and even though the CPU : system power ratio did not change, leakage (static) becoming more and more dominant changes the ratio between the 3 drastically.

## Slide 27: Balancing Computation and I/O
DVFS can improve energy efficiency
  when speed is not sacrificed
Bring program to compute-I/O balanced state
  If it’s memory-bound, slow down CPU
  If it’s compute-bound, slow down memory
Still maximizing hardware utilization
  but by lowering the hardware capability
Current hardware (e.g., Intel Turbo-boost) and/or OS do this for processor
Notes: You can see various compiler optimizations to improve hardware utilization; DVFS for energy is the other side of the picture that can bring down the “max”.
This is really how DVFS should be viewed/used.

## Slide 28: Thank you!